## Slide 1: Neuromorphic Computing Paper Review
Dave Cheng
2/20/2018

## Slide 2: Papers about Stochastic Computing

## Slide 3: Preliminary
What is the basic concept of Stochastic Computing (SC)?
  SC is a paradigm that represents a probabilistic number by counting the number of ones in a bit-stream.
  Consider this bit-stream 0100110100 ->4 1s out of 10 bits. 4/10 = 0.4
  We use the above bit-stream to represent the number between [0,1]
  Question1: How many 1s do we need to represent 0.4 in the range of [-1, 1]?

## Slide 4: Research Motivation
SC-DCNN: Stochastic Computing + Deep Convolutional Neural Network
High scalability and ultra-low hardware footprint
  0100110100 = 01100
Conventional multiplier
SC multiplier
Notes: What the problem that the author tries to solve

## Slide 5: Technical contributions
Applying SC to DCNNs
Hardware oriented design.
  Weight storage
  proposed a Approximate parallel counter (APC)-based method for basic operation.
    Question 2:
00100101
11001010
11101111
10011000
11001010
3/8
4/8
7/8
3/8
4/8
or
or
11011010 5/8
rescale to make sure very few 1’s in the bit-streams

## Slide 6: Technical contributions
APC-based inner product
  number of inputs is n. length of a bit-stream is m
  the products of x’s and w’s can be represented by a bit-matrix of size [n, m] .
  count the number of ones in each column and represent the result in the binary format.
  40% reduction of gatecount.
Notes: Log2 16
log2n m.

## Slide 7: Technical contributions
Avg pooling causes more information loss than the hardware-oriented max pooling.
  the fractional part of the number after average pooling is dropped
  Ex: mean (2, 3, 4, 5) = 3.5 = 3 (binary)
  Question3: What method will you propose?

## Slide 8: Experimental Results
Save storage from weight, inner product.
ASIC:Image/sec/area or Image/sec/watt
GPU: Image/sec

## Slide 9: Q&A
Thank you for listening!